## Slide 1: RTS1 Week 1

## Slide 2: Leerdoelen Week 1 Theoriedeel
Leerdoelen week 1 theoriedeel. Je leert:
de ARM Cortex processor familie kennen;
een vereenvoudigde versie van de ARMv7-M architectuur, de LEGv7-M architectuur, kennen;
een vereenvoudigde versie van de Thumb instructieset, de Pinky instructieset, kennen;
assembleertaalprogramma’s te schrijven in Pinky;
Pinky assembly om te zetten naar machinecode (encoden);
Pinky machinecode om te zetten naar assembly (decoden).
Studiemateriaal: De LEGv7 architectuur en de Pinky instructieset

## Slide 3: ARM Cortex Processor Family

## Slide 4: Source Reference
The material in this presentation is inspired by chapter 2 of the book:
  Computer Organization and Design
    The Hardware / Software Interface
      ARM Edition
      David A. Patterson, John L. Hennessy
      ISBN: 9780128017333
Main differences:
  The book uses ARMv8 Cortex-A , I use ARMv7 Cortex-M
  The book uses ARM instructions, I use Thumb instructions

## Slide 5: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 6: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 7: Instructions: The language of the computer
  How to tell a computer what to do?
  Bits are the letters of the computer
  Instructions are the words of the computer
    An instruction is a collection of bits
  The instruction set is the vocabulary of the computer
    An instruction set is a collection of instructions

## Slide 8: Instruction Set
  The repertoire of instructions of a computer
  Different computers have different instruction sets
    But with many aspects in common

## Slide 9: The ARMv7 Thumb Instruction Set
  A subset, called LEGv7 Pinky, used as the example throughout these lessons
  Commercialized by ARM Holdings (www.arm.com)
  Large share of embedded core market
    Applications in consumer electronics, network/storage equipment, cameras, printers, …
  Typical of many modern ISAs
    See De LEGv7 architectuur en de Pinky instructieset

## Slide 10: Levels of Program Code
  High-level language
    Level of abstraction closer to problem domain
    Provides for productivity and portability
  Assembly language
    Textual representation of instructions
  Hardware representation
    Binary digits (bits)
    Encoded instructions and data

## Slide 11: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
Supporting Functions in Computer Hardware
LEGv7 Addressing for 32-bits Literals

## Slide 12: Arithmetic Operations
  Add and subtract, three operands
    Two sources and one destination
  ADDS.N a, b, c // a gets b + c SUBS.N a, b, c // a gets b - c
  S means that the instruction is updating condition flags (N = Negative, Z = Zero, V = oVerflow, C = Carry) in the Program Status Register
  N means Narrow (16-bits instruction)

## Slide 13: Arithmetic Example
C code:
f = (g + h) - (i - h);
Compiled LEGv7 Pinky code:
ADDS.N t0, g, h SUBS.N t1, i, h SUBS.N f, t0, t1
Processor does not work with variables but with registers

## Slide 14: Memory Hierarchy
The ALU can only operate on values that are inside the registers
Not directly from the main memory!
Need to LOAD stuff from main memory

## Slide 15: Register Operands
  Arithmetic instructions use register operands
  LEGv7 has an 8 × 32-bits register file
    Use for frequently accessed data
    32-bits data is called a “word”
      8 x 32-bits general purpose registers R0 to R7

## Slide 16: LEGv8 Registers

## Slide 17: Program Status Register
  Consists of three overlapping registers
    Application Program Status Register (APSR)
    Interrupt Program Status Register (IPSR)
    Execution Program Status Register (EPSR)
  T bit indicates that Thumb (Pinky) instructions are executed

## Slide 18: Arithmetic Example
C code:
f = (g + h) - (i - h);
  f, g, h, i in R4, R5, R6, R7
Compiled LEGv7 Pinky code:
ADDS.N R0, R5, R6 SUBS.N R1, R7, R6 SUBS.N R4, R0, R1

## Slide 19: Arithmetic Example (Alternative)
C code:
f = (g + h) - (i - h);
  f, g, h, i in R4, R5, R6, R7
Compiled LEGv7 Pinky code:
ADDS.N R4, R5, R6 SUBS.N R4, R4, R7 ADDS.N R4, R4, R6
No temporary use of registers needed

## Slide 20: Memory Operands
  Main memory used for composite data
    Arrays, structures, dynamic data
  To apply operations
    Load values from memory into registers
    Store result from register to memory
  Memory is byte addressed
    Each address identifies an 8-bit byte
  LEGv7 does not require words to be aligned in memory, except for instructions (must be halfword aligned) and the stack (must be word aligned)
    But unaligned loads/stores take 2 (halfword, not word aligned) or 3 (not halfword aligned) clock cycles extra

## Slide 21: Load / Store instructions
#<imm7> is a 7-bits unsigned immediate offset (0 t/m 127) that is dividable by 4

## Slide 22: Arithmetic Example (Alternative)
C code:
int a[] = {1,2,3,4,5,6,7,8,9}; a[8] = h + a[3];
  h in R4, base address of a in R5
Compiled LEGv7 Pinky code:
LDR.N R0, [R5, #12] ADDS.N R1, R4, R0 STR.N R1, [R5, #32]

## Slide 23: Registers versus Memory
  Registers are faster to access than memory
  Operating on memory data requires loads and stores
    More instructions to be executed
  Compiler must use registers for variables as much as possible
    Only spill to memory for less frequently used variables
    Register optimization is important!

## Slide 24: Immediate Operands
  Constant data specified in an instruction
    <imm3> = 0 t/m 7, <imm8> = 0 t/m 255
  Make the common case fast
    Small constants are common
    Immediate operand avoids a load instruction

## Slide 25: Signed and Unsigned Numbers
  I skip this part of the lecture because I assume you already now this stuff.
  You maybe have to study it yourself!

## Slide 26: Unsigned Binary Integers
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
>>

## Slide 27: 2s-Complement Signed Integers
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647
>>

## Slide 28: 2s-Complement Signed Integers
  Bit 31 is sign bit
    1 for negative numbers
    0 for non-negative numbers
  –(–2n – 1) can’t be represented
  Non-negative numbers have the same unsigned and 2s-complement representation
  Some specific numbers
    0: 0000 0000 … 0000
    –1: 1111 1111 … 1111
    Most-negative: 1000 0000 … 0000
    Most-positive: 0111 1111 … 1111
>>

## Slide 29: Signed Negation
  Complement and add 1
    Complement means 1 → 0, 0 → 1
>>
  Example: negate +2
    +2 = 0000 0000 … 0010two
    –2 = 1111 1111 … 1101two + 1 –2 = 1111 1111 … 1110two

## Slide 30: Sign Extension
  Representing a number using more bits
    Preserve the numeric value
  Replicate the sign bit to the left
    c.f. unsigned values: extend with 0s
  Examples: 8-bit to 16-bit
    +2: 0000 0010 => 0000 0000 0000 0010
    –2: 1111 1110 => 1111 1111 1111 1110
>>

## Slide 31: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 32: Representing Instructions
  Instructions are encoded in binary
    Called machine code
  LEGv7 Pinky instructions
    Encoded as 16-bit instruction words
    Small number of formats encoding operation code (opcode), register numbers, …
    Regularity!

## Slide 33: Hexadecimal
  Base 16
    Compact representation of bit strings
    4 bits per hex digit
>>
0 | 0000 | 4 | 0100 | 8 | 1000 | C | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | D | 1101
2 | 0010 | 6 | 0110 | A | 1010 | E | 1110
3 | 0011 | 7 | 0111 | B | 1011 | F | 1111
  Example: ECA8
    1110 1100 1010 1000

## Slide 34: Arithmetic instructions encoding
  Instruction fields
    Opcode (b15 – b9): operation code
    Rm (b8 – b6): the second register source operand
    Rn (b5 – b3): the first register source operand
    Rd (b2 – b0): the register destination

## Slide 35: Arithmetic instructions encoding
  Encode into LEGv7 machine language:
  ADDS.N R0, R5, R6 SUBS.N R1, R7, R6 SUBS.N R4, R0, R1

## Slide 36: Load / Store instructions encoding
Rn: base register
Rt: destination (load) or source (store) register
#<imm7> is a 7-bits unsigned immediate offset (0 t/m 127) that must be divisble by 4
imm5 = <imm7> / 4

## Slide 37: Load / Store instructions encoding
  Encode into LEGv7 machine language:
  LDR.N R0, [R5, #12] ADDS.N R1, R4, R0 STR.N R1, [R5, #32]

## Slide 38: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 39: Logical Operations
  Instructions for bitwise manipulation
Operation | C | LEGv7 Pinky
Shift left | << | LSLS.N
Shift right | >> (unsigned) | LSRS.N
Bit-by-bit AND | & | ANDS.N
Bit-by-bit OR | ¦ | ORRS.N
Bit-by-bit EXOR | ^ | EORS.N
  Useful for extracting and inserting groups of bits in a word

## Slide 40: Shift Operations
  <imm5>: (0 – 31) how many positions to shift
  Shift left logical
    Shift left and fill with 0 bits, shift through C-flag
    LSL by i bits multiplies by 2i
  Shift right logical
    Shift right and fill with 0 bits, shift through C-flag
    LSR by i bits divides by 2i (unsigned only)

## Slide 41: Logical Bitwise Operations

## Slide 42: AND Operations
  Useful to mask bits in a word
    Set some bits to 0, leave others unchanged
  ANDS.N R4,R5
01010101 10101010 00110011 11001100
R4
R5
R4
11111111 00000000 00000000 11110000
01010101 00000000 00000000 11000000
>>

## Slide 43: OR Operations
  Useful to include bits in a word
    Set some bits to 1, leave others unchanged
  ORRS.N R4,R5
01010101 10101010 00110011 11001100
R4
R5
R4
11111111 00000000 00000000 11110000
11111111 10101010 00110011 11111100
>>

## Slide 44: EOR Operations
  Differencing operation
    Invert (flip) some bits, leave others unchanged
  EORS.N R4,R5
01010101 10101010 00110011 11001100
R4
R5
R4
11111111 00000000 00000000 11110000
10101010 10101010 00110011 00111100
>>

## Slide 45: Shift Example
C code:
// f = (g + h) - (i - h); f = g + 2*h - i;
  f, g, h, i in R4, R5, R6, R7
Compiled LEGv7 Pinky code:
LSLS.N R0, R6, #1 ADDS.N R1, R5, R0 SUBS.N R4, R1, R7

## Slide 46: Move Instruction
MOVS.N <Rd>, <Rm> Is encoded as: LSLS.N <Rd>, <Rm>, #0
MOVS.N <Rd>, <Rm> is a pseudo instruction
It doesn’t have its own machine code

## Slide 47: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 48: Conditional Operations
  Branch to a labeled instruction if a condition is true
    Otherwise, continue sequentially
  CBZ.N register, L1
    if (register == 0) branch forward to instruction labeled L1:
  CBNZ.N register, L1
    if (register != 0) branch forward to instruction labeled L1:
  B.N L1
    branch unconditionally to instruction labeled L1:
CBZ = Compare and Branch if Zero

## Slide 49: Compiling If Statements
  C code:
  if (h == i) f = g + 3; else f = f - 17;
    f, g, h, i in R4, R5, R6, R7
Compiled LEGv7 Pinky code:
SUBS.N R0, R6, R7 CBNZ.N R0, else ADDS.N R4, R5, #3 B.N endif else: SUBS.N R4, #17 endif:
Assembler calculates offsets
Branch is performed by adding an offset to PC

## Slide 50: Encoding Branch Instructions
Encode the following LEGv7 Pinky code:
SUBS.N R0, R6, R7 CBNZ.N R0, else ADDS.N R4, R5, #3 B.N endif else: SUBS.N R4, #17 endif:
See Appendix B De LEGv7 architectuur en de Pinky instructieset

## Slide 51: Compiling Loop Statements
  C code:
  int i = 0; while (save[i] == k) i += 1;
    i in R4, k in R5, address of save in R6
Compiled LEGv7 Pinky code:
MOVS.N R4, #0 while: LSLS.N R0, R4, #2 LDR.N R1, [R6, R0] SUBS.N R2, R1, R5 CBNZ.N R2, endwhile ADDS.N R4, R4, #1 B.N while endwhile:
Assembler calculates offsets
Branch is performed by adding an offset to PC

## Slide 52: Better Compiling Loop Statements
  C code:
  int i = 0; while (save[i] == k) i += 1;
    i in R4, k in R5, address of save in R6
Compiled LEGv7 Pinky code:
MOVS.N R4, #0 while: LDR.N R0, [R6, R4] SUBS.N R1, R0, R5 CBNZ.N R1, endwhile ADDS.N R4, R4, #4 B.N while endwhile: LSRS.N R4, #2
One less instruction in loop

## Slide 53: More Conditional Operations
  Condition codes, set from instruction with S-suffix (ADDS, ANDS, SUBS, ….)
    negative (N): result had 1 in MSB
    zero (Z): result was 0
    overflow (V): result sign overflowed
    carry (C): result had carryout from MSB
  Use CMP.N, then conditionally branch:
    B.EQ (equal)
    B.NE (not equal)
    B.LT (less than, < signed), B.LO (lower, < unsigned)
    B.LE (less than or equal, ≤ signed), B.LS (lower or same, ≤ unsigned)
    B.GT (greater than, > signed), B.HI (higher, > unsigned)
    B.GE (greater than or equal, ≥ signed), B.HS (higher or same, ≥ unsigned)
CMPS.N would have been a better name

## Slide 54: Signed versus Unsigned
  Signed comparison ≠ Unsigned comparison
  Example
    R0 = 1111 1111 1111 1111 1111 1111 1111 1111
    R1 = 0000 0000 0000 0000 0000 0000 0000 0001
    R0 ? R1 signed
      –1 < +1
    R0 ? R1 unsigned
      +4294967295 > +1
<
>

## Slide 55: B<c>.N condities

## Slide 56: Conditional Example
C code:
int a, b; if (a > b) a += 1;
  a, b in R4, R5
Compiled LEGv7 Pinky code:
CMP.N R4, R5 BLE.N exit ADDS.N R4, #1 exit:
Note: condition in B<c>.N is complement of condition in if

## Slide 57: Conditional Example
C code:
unsigned int a, b; if (a > b) a += 1;
  a, b in R4, R5
Compiled LEGv7 Pinky code:
CMP.N R4, R5 BLS.N exit ADDS.N R4, #1 exit:

## Slide 58: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 59: Load 32-bit literal in register
MOVS.N Rd, #<imm8> can be used to load an 8-bits unsigned constant in Rd.
How to load a 32-bits constant in Rd with a 16-bits instruction?
Literal addressing mode:
  LDR.N R6, =0x1234567
Is encoded as:
  LDR.N R6, [PC, #offset] //... .word 0x1234567 // literal section
Note: offset is 10-bits unsigned which should be dividable by 4
Instead of a constant, a label can be used (to load an address)

## Slide 60: Agenda
Instruction Set
Operations and Operands
Representing Instructions in the Computer
Logical Operations
Instructions for Making Decisions
LEGv7 Addressing for 32-bits Literals
Supporting Functions in Computer Hardware

## Slide 61: Subroutine (Function) Calling
Steps required:
Place parameters in registers R0 to R3
Transfer control to function
Acquire local storage for function
Perform function’s operations
Place result in register R0 for caller
Return to place of call (address in LR)

## Slide 62: Function Call Instructions
  Function call: Branch with Link and eXchange LDR.N R4, =FunctionLabel BLX.N R4
    Address of following instruction put in LR (Link Register)
    Jumps to target address
  Function return: Branch and eXchange BX.N LR
  Copies LR to program counter
    Can also be used for computed jumps
      e.g., for case/switch statements or jump to function pointers

## Slide 63: T-bit
When the PC is loaded (e.g. by BLX or BX) bit 0 is copied to the T-bit.
This way the processor can switch (eXchange) between the Thumb and ARM instruction sets.
ARM Cortex-M only supports Thumb and raises an exception when T is 0.

## Slide 64: Register Usage
  R0 to R3: temporary registers
    Used to pass arguments to functions and pass return value
    Not preserved by the callee
  R4 to R7: saved registers
    If used, the callee saves and restores them
Callee = function which is called
ARM Call Convention
Should we follow this convention?

## Slide 65: Leaf Function Example
  C code:
  int leaf_example(int g, int h, int i, int j) { int f; f = (g + h) - (i - j); return f; }
Compiled LEGv7 Pinky code:
.thumb_func leaf_example: ADDS.N R0, R0, R1 SUBS.N R2, R2, R3 SUBS.N R0, R0, R2 BX.N LR

## Slide 66: Leaf Function Example
  C code:
  int leaf_example(int g, int h, int i, int j) { int f; f = (g + h) - (i - j); return f; }
Compiled LEGv7 Pinky code:
.thumb_func leaf_example: ADDS.N A1, A1, A2 SUBS.N A3, A3, A4 SUBS.N A1, A1, A3 BX.N LR
R0 to R3 may also be called A1 to A4

## Slide 67: Leaf Function Call Example
  C code:
  int a, b, c, d; //... a = leaf_example(b, c, d, c);
    a to d in R4 to R7
Compiled LEGv7 Pinky code:
MOVS.N R0, R5 MOVS.N R1, R6 MOVS.N R2, R7 MOVS.N R3, R6 LDR.N R4, =leaf_example BLX.N R4 MOVS.N R4, R0

## Slide 68: Leaf Function Call Example
  C code:
  int a, b, c, d; //... a = leaf_example(b, c, d, c);
    a to d in R4 to R7 (V1 to V4)
Compiled LEGv7 Pinky code:
MOVS.N A1, V2 MOVS.N A2, V3 MOVS.N A3, V4 MOVS.N A4, V3 LDR.N V1, =leaf_example BLX.N V1 MOVS.N V1, A1
R4 to R7 may also be called V1 to V4

## Slide 69: Leaf Function Example
  C code:
  int leaf_example(int g, int h, int i, int j) { int f = (g + h) - (i + j); // more code which needs g, h, i and j return f; }
Compiled LEGv7 Pinky code:
.thumb_func leaf_example: ADDS.N R4, R0, R1 SUBS.N R5, R2, R3 // more code which needs R0, R1, R2 and R3 SUBS.N R0, R4, R5 BX.N LR
Does not conform to ARM ABI
Where to temporary store R4 and R5?
What’s wrong?

## Slide 70: Local Data on the Stack
Before function call
During function call
After function call

## Slide 71: Leaf Function Example
Compiled LEGv7 Pinky code:
.thumb_func leaf_example: PUSH.N {R4, R5} ADDS.N R4, R0, R1 SUBS.N R5, R2, R3 // more code which needs R0, R1, R2 and R3 SUBS.N R0, R4, R5 POP.N {R4, R5} BX.N LR

## Slide 72: Leaf Function Example
  C code:
  unsigned int gcd(unsigned int a, unsigned int b) { while (a != b) { if (a > b) { a = a – b; } else { b = b – a; } } return a; }
Compiled LEGv7 Pinky code:
https://en.wikipedia.org/wiki/Euclidean_algorithm

## Slide 73: Leaf Function Example
Compiled LEGv7 Pinky code:
.thumb_func gcd: CMP.N R0, R1 BEQ.N end BLS.N else SUBS.N R0, R0, R1 B.N gcd else: SUBS.N R1, R1, R0 B.N gcd end: BX.N LR

## Slide 74: Non-Leaf Function Example
  C code:
  bool is_coprime(unsigned int a, unsigned int b) { return gcd(a, b) == 1; }
Compiled LEGv7 Pinky code:
.thumb_func is_coprime: LDR.N R2, =gcd PUSH.N {LR} BLX.N R2 CMP.N R0, #1 BEQ.N end MOVS.N R0, #0 end: POP.N {PC}
https://en.wikipedia.org/wiki/Coprime_integers

## Slide 75: More examples to study @Home

## Slide 76: Encoding Functions
Encode the following LEGv7 Pinky code:
LDR.N R4, =leaf_example BLX.N R4 MOVS.N R4, R0 end: B.N end .thumb_func leaf_example: ADDS.N R0, R0, R1 SUBS.N R2, R2, R3 SUBS.N R0, R0, R2 BX.N LR
See Appendix B De LEGv7 architectuur en de Pinky instructieset

## Slide 77: Decode
Decode the following LEGv7 Pinky machine code
0110100000000011
0110100000001010
0110000000000010
0110000000001011
0100011101110000
See Appendix C De LEGv7 architectuur en de Pinky instructieset
Can you guess which function this is?

## Slide 78: Decode
Decode the following LEGv7 Pinky machine code
1bf0
b908
1cec
e001
002c
3c11
See Appendix C De LEGv7 architectuur en de Pinky instructieset

## Slide 79: Recursive Function Example
  C code:
  unsigned int fib(unsigned int n) { if (n < 2) { return n; } return fib(n-1) + fib(n-2); }
Compiled LEGv7 Pinky code:
https://en.wikipedia.org/wiki/Fibonacci_number

## Slide 80: Recursive Function Example
.thumb_func fib: CMP.N R0, #2 BHS.N endif BX.N LR endif: PUSH.N {R4, R5, R6, LR} LDR.N R4, =fib MOVS.N R5, R0 SUBS.N R0, #1 BLX.N R4 MOVS.N R6, R0 MOVS.N R0, R5 SUBS.N R0, #2 BLX.N R4 ADDS.N R0, R0, R6 POP.N {R4, R5, R6, PC}
372135 clock cycles to calculate fib(20)

## Slide 81: Recursive Function Example
.thumb_func fib: LDR.N R1, =fib_r .thumb_func fib2_r: CMP.N R0, #2 BHS.N endif BX.N LR endif: PUSH.N {R0, R4, LR} SUBS.N R0, #1 BLX.N R1 MOVS.N R2, R0 LDR.N R0, [SP, #0] SUBS.N R0, #2 BLX.N R1 ADDS.N R0, R0, R2 POP.N {R2, R4, PC} // R2 is dummy
328357 clock cycles to calculate fib(20)

## Slide 82: Better Non-Recursive fib(n)
.thumb_func fib: CMP.N R0, #2 BLO.N end endif: SUBS.N R3, R0, #1 MOVS.N R2, #0 MOVS.N R1, #1 loop: ADDS.N R0, R1, R2 MOVS.N R2, R1 MOVS.N R1, R0 SUBS.N R3, #1 BNE.N loop end: BX.N LR
121 clock cycles to calculate fib(20)
Geef de C code voor unsigned int fib(unsigned int n)

## Slide 83: Volgende les…
Theorie:
Hardware implementatie van een vereenvoudigde versie van de LEGv7-M architectuur
Deze implementatie versnellen door het toepassen van:
  een pipeline
  branch prediction
  cache geheugen
Lab:
Aansturen van leds op verschillende abstractieniveaus.

## Slide 84: Aan de slag!
Aan de slag met Opdrachten_Week_1.pdf