## Slide 1: RTS1 Week 4

## Slide 2: Planning RTS1
Week 3: Cooperative Scheduling
Week 4: Pre-emptive Scheduling
Week 5: Using an RTOS
Week 6: Schedulability Analyses, Priority Assignment
Week 7/8: Introduction (embedded) Rust

## Slide 3: Overview
Scheduling
  Problem
  Goal
  Possible solution

## Slide 4: Scheduling
Problem
  Multiple processes require CPU time
    Some processes need it asap
    Some processes just need to happen at some point in time
  Multiple processes require bandwidth
    USB, Serial, SPI ....
    Prioritization?
Goal
  Create a framework that’ll ease (CPU) time management
  Easy to add new processes and to share resources

## Slide 5: Demo
Demonstration of pre-emptive project

## Slide 6: Cooperative versus Pre-emptive scheduling
Cooperative
  Tasks run sequentially
  High priority tasks have to wait till last task finishes
  Easy to set up
  Low overhead scheduler
Pre-emptive (Multi-tasking)
  Important tasks always finish first
  Danger of starvation and using hardware concurrently
  More overhead on resources(RAM) and CPU time

## Slide 7: Embedded system example
T
S
P
Switch
Screen
DAC
ADC
ADC
thermocouple
pressure transducer
heater
pump/valve

## Slide 8: Pre-emption
Interrupting a task to execute a different task
Cooperative Preemptive
Scheduler decides next task and can interrupt existing
Context switch, switches the tasks
T
P
S
T
P
S

## Slide 9: Context switch
What is context?
  What memory is used by code?
    Stack
    Heap (dynamic memory)
    CPU registers
Stack and CPU registers describe the context of a task

## Slide 10: OS support in Cortex M4
Banked stack pointers
Privileged and non-privileged operation modes
Advanced interrupt controller (NVIC)
  Has several interrupts specifically for RT kernels
  Fault handlers
Memory Protection Unit (MPU)

## Slide 11: Banked stack pointers
R13 can contain
  the Process Stack Pointer (PSP)
  the Main Stack Pointer (MSP)
MSP is default
PSP can be used for separating tasks from the OS
  Normal tasks do not share their stack with the kernel! Much safer.
  Can only be used outside of interrupts
  Set using SPSEL bit in CONTROL register
Thus far all we have used is the MSP

## Slide 12: Memory usage in a RTOS
Each task gets own chunk of memory
  The OS uses the MSP
  The tasks use the PSP
    When a new task is selected, the PSP points to the stack of that task.
    Basically, a form of ‘Time division multiplexing’
    The scheduling algorithm picks the next task/stack
OS/SysTick
MSP
Task1
PSP
Task2
PSP
Task3
PSP
OS/SysTick
MSP
OS
Task 1
Task 2
Task N
MSP
PSP

## Slide 13: Banked stack pointers
Two assembly instructions for accessing special registers
  MRS (move special register value to normal register)
    E.g. MRS R0, PSP ; move PSP value to R0
  MSR (Move normal register value to special register)
    E.g. MSR PSP, R0 ; move R0 value to PSP
And CMSIS functions
  __get_PSP(void)
  __set_PSP(uint32_t topOfStack)

## Slide 14: Exception entry
On exception several registers are automatically pushed to the current stack pointer
The CPU writes an EXC_RETURN value to the LR which determines if the MSP or PSP stack was in use
C functions are allowed to use R0-R3 and R12 inside an exception.

## Slide 15: Exception return
The CPU checks the EXC_RETURN value in the LR which determines if the MSP or PSP stack is used
The CPU pops the stackframe from the MSP or PSP
The stack used determines the value for the program counter and link register and thus where code execution continues

## Slide 16: Exception flowchart
Exception entry
SP
LR = 0xFFFFFFFD
push stack frame to SP
LR = 0xFFFFFFF9
MSP
PSP
SP = MSP
LR
0xFFFFFFF9
0xFFFFFFFD
pop stack frame from MSP
pop stack frame from PSP
Exception return
run ISR

## Slide 17: Example OS
OS/SysTick
MSP
Init
MSP
Task1
PSP
Task2
PSP
OS/SysTick
MSP
LR = EXC_RETURN_MSP
LR = EXC_RETURN_PSP

## Slide 18: Operation modes
Security by:
  Separating stacks
  Separating access levels between kernel and tasks.
    nPRIV bit in CONTROL register
Handler mode
  Used by exceptions
Privileged Thread mode
  OS intialisation
  OS kernel
Unprivileged Thread mode
  Used by tasks
  Tasks have limited access to memory
  MPU can be used to change access
Handler mode
privileged
Thread mode
privileged
Thread mode
unprivileged
Interrupt request
Interrupt request
Return
with MSP or PSP
Uses MSP
nPRIV = 0
nPRIV = 1
nPRIV = 1

## Slide 19: Operation modes
Abstraction
  Only OS can access important peripherals like Systick, NVIC, DMA, MPU, etc
  Tasks need to use the OS system calls to request changes
SVC Handler
Drivers
Kernel
Tasks
Important Peripherals
Unprivileged
privileged

## Slide 20: OS Interrupts
Systick
  Used by OS to periodically update everything
PendSV (Pendable Service Call)
  Used by OS to request a context switch
  Software bit triggers this interrupt
  Lowest priority
SVC (SuperVisor Call)
  Used by tasks to request a service from the OS

## Slide 21: Supervisor call
Assembly call
  SVC #x
    Parameter X defines which action the OS performs, first byte of instruction
    Interrupt occurs immediately
    You can get and return parameters with stacked registers like normal function call
Exception entry
Use PC to find used instruction
Check used stack pointer
Get parameter from first byte of instruction

## Slide 22: PendSV - Context switch
R0-R3,R12,LR,PC,XPSr get pushed to current stack
Push {R4-R11} CPU registers to PSP, update stack pointer
Pick new task and change PSP
Pop {R4-R11} from new PSP, update stack pointer
R0-R3,R12,LR,PC,XPSr get popped from current stack

## Slide 23: Switching context
save context ->
Enter exception (PendSV)
Save context (CPU registers) to stack
Switch stack to new task
Load context from stack to CPU
Leave exception using new stack

## Slide 24: Memory Protection Unit
Can set memory locations
  Inaccessible
  Read only
  Non-executable
Possible use-case in RTOS
  Limit access to certain peripherals
  Only allow access to own task memory (and thus stack)
    Downside?
  Make RAM segments non-executable to prevent injection-type attacks
FreeRTOS-MPU - ARM Cortex-M3 and ARM Cortex-M4 Memory Protection Unit support in FreeRTOS
Why ARM MPU Has Become an Outcast in Embedded Systems

## Slide 25: Pre-emptive scheduling
Priority based
  Scheduler decides and update states of tasks
  When high priority task comes alive, it interrupts lower priority tasks
  When all tasks are suspended, the idle task can run
Round robin
  Every task gets equal CPU time
  When all tasks are suspended, the idle task can run
Demo
  Instructor demonstrates algorithms

## Slide 26: Problems with pre-emptive scheduling
Starvation
  Low priority tasks don’t get cpu time
    Possible solution: Aging
Sharing resources
  Tasks can’t use hardware ‘simultaneously’
  Waiting for hardware to come available can cause deadlock or priority inversion
    Next week

## Slide 27: Walkthrough VersdOS

## Slide 28: Next Week
Free-RTOS
  What is it
  Problems and challenges with
  Threads and IPC (Inter Process Synchronization)
  POSIX API overview
  Read assignment 5 before next week’s lesson!

## Slide 29: Aan de slag!
Aan de slag met Opdrachten_Week_4.pdf